## Slide 1
RFID Manager
Test Setup — Overview
MQTT Infrastructure • NFC Scanning • End-to-End Testing
2026-06-14

## Slide 2
System Overview
Full architecture from NFC scan to data persistence
📱 Android App (RFID Manager)
• NFC Reader/Writer • MQTT Client (Paho) • Room DB (local cache) • Scan → Publish flow • IP: 192.168.50.112 • WiFi-connected
🌐 MQTT Broker (Mosquitto)
• Docker container • eclipse-mosquitto:latest • Port 1883 (TCP) • allow_anonymous: true • IP: 192.168.50.128 • Mosquitto 2.1.2
💾 Subscriber / Backend
• Python subscriber script • SQLite persistence • Filters: rfidmanager/+/telemetry • Color-coded terminal output • Statistics on exit • Localhost connection
🔁 Data Flow
1. NFC-tag scanned → UID extracted 2. JSON payload constructed 3. Published to rfidmanager/<uid>/telemetry 4. Broker routes to all subscribers 5. Python subscriber logs to SQLite 6. App stores locally in Room DB
🧪 Test Configuration
• Broker: 192.168.50.128:1883 • Topic: rfidmanager/<uid>/telemetry • QoS: 1 (at least once) • Keep-alive: 30s • cleanSession: true • JSON format payload

## Slide 3
MQTT Infrastructure
Publish/Subscribe pattern — decoupled architecture
Publish / Subscribe Model
┌─────────────┐ ┌─────────────┐ │ Publisher │ │ Publisher │ │ (App) │ │ (Simulator)│ └──────┬──────┘ └──────┬──────┘ │ │ ▼ ▼ ┌─────────────────────────────────┐ │ MQTT BROKER (Mosquitto) │ │ 192.168.50.128:1883 │ └────────┬────────────────┬────────┘ │ │ ▼ ▼ ┌─────────────┐ ┌─────────────┐ │ Subscriber │ │ Subscriber │ │ (Python) │ │ (MQTT Exp) │ │ → SQLite │ │ → GUI view │ └─────────────┘ └─────────────┘ Key points: • Publishers don't know subscribers • Broker handles all routing • Any number of pub/sub on each topic • Wildcards enable flexible subscriptions
Topic Structure
rfidmanager / <uid> / telemetry ↑ ↑ ↑ our app tag ID data type Examples: • rfidmanager/047B1234/telemetry • rfidmanager/0A1B2C3D/telemetry Wildcards: • rfidmanager/# — all messages • rfidmanager/+/telemetry — all UIDs • rfidmanager/047B1234/+ — all types JSON Payload: {"uid":"047B1234","type":"rfid", "timestamp":1718300000} QoS Levels: • 0: fire-and-forget • 1: at least once (our choice) • 2: exactly once (overkill)

## Slide 4
Network Topology
Home network: 192.168.50.0/24
📱 Phone (WiFi)
• Samsung Galaxy Note 10 • IP: 192.168.50.112 • Paho MQTT Client • clientId: rfid-android-client • Publishes on scan
💻 PC — Docker Host
• IP: 192.168.50.128 • Mosquitto container (port 1883) • Python subscriber • MQTT Explorer • All on same machine
🌍 External Tools
• mosquitto_pub/sub (standalone or via docker) • MQTT Explorer (GUI) • Wireshark (packet analysis) • netcat (raw TCP test)
Connection Matrix
┌──────────────────────────────────────────────────────────────────────────────┐ │ Component │ IP/Host │ Connects To │ Port │ Protocol │ ├──────────────────────────────────────────────────────────────────────────────┤ │ Phone (App) │ 192.168.50.112 │ Broker (WiFi) │ 1883 │ MQTT │ │ Broker (Container) │ 192.168.50.128 │ — (accepts all) │ 1883 │ TCP │ │ Python Subscriber │ localhost │ Broker (local) │ 1883 │ MQTT │ │ MQTT Explorer │ 192.168.50.128 │ Broker │ 1883 │ MQTT │ │ mosquitto CLI │ localhost/192.168.50.128 │ Broker │ 1883 │ MQTT │ │ Wireshark │ any │ Network interface │ — │ MQTT ftr │ └──────────────────────────────────────────────────────────────────────────────┘

## Slide 5
Test Tools & Commands
Three ways to test — CLI, Docker, or GUI
🔧 Method 1: Standalone mosquitto CLI
Install: sudo pacman -S mosquitto Listen on all topics: mosquitto_sub -h 192.168.50.128 -p 1883 \ -t "rfidmanager/#" -v Publish test message: mosquitto_pub -h 192.168.50.128 -p 1883 \ -t "rfidmanager/test/telemetry" \ -m '{"uid":"test"}'
🐳 Method 2: Via Docker container
No installation needed — broker already has mosquitto tools. Listen: docker exec rfid-mqtt-test mosquitto_sub \ -h localhost -p 1883 -t "rfidmanager/#" -v Publish: docker exec rfid-mqtt-test mosquitto_pub \ -h localhost -p 1883 \ -t "rfidmanager/test/telemetry" \ -m '{"type":"test"}'
🖥️ Method 3: MQTT Explorer (GUI)
Download: github.com/thomasnordquist/MQTT-Explorer Connection settings: Host: 192.168.50.128 Port: 1883 SSL/TLS: Off Auth: None Subscribe to rfidmanager/# for real-time view
🐍 Python Test Scripts
Location: ~/rfid-manager/test/fas2-mqtt/mqtt/ Subscriber (SQLite logging): ./test_subscriber_persist.py ./test_subscriber_persist.py --uid 047B Simulator (simulate phone): ./simulate_mobile_publish.py Output: ~/rfid-manager/data/rfid_readings.db

## Slide 6
Broker Administration
Docker-based Mosquitto management
Docker Commands
┌─────────────────────────────────────────────────────────────┐ │ Command │ Description │ ├─────────────────────────────────────────────────────────────┤ │ docker run ... eclipse-mosquitto │ Start broker (--rm!) │ │ docker start rfid-mqtt-test │ Start existing cont. │ │ docker stop rfid-mqtt-test │ Stop broker │ │ docker restart rfid-mqtt-test │ Restart broker │ │ docker ps --filter name=rfid-... │ Check if running │ │ docker logs rfid-mqtt-test │ View logs │ │ docker logs -f rfid-mqtt-test │ Follow logs live │ │ docker exec -it rfid-mqtt-test sh │ Shell inside container │ │ docker inspect rfid-mqtt-test │ Detailed info │ └─────────────────────────────────────────────────────────────┘ ⚠️ The container uses --rm: it is deleted on stop. You must run 'docker run' again, not 'docker start'. Omit --rm if you want persistent container lifecycle.
mosquitto.conf
File: ~/rfid-manager/test/fas2-mqtt/mqtt/mosquitto.conf Config: listener 1883 # MQTT port allow_anonymous true # No auth required persistence true # Data saved to disk persistence_location # /mosquitto/data/ log_dest stdout # Logs to console Not configured (defaults): • max_connections: unlimited • keepalive_interval: 60s • allow_zero_length_clientid: true Logs show: • New connections (IP + port) • Client IDs • Disconnections

## Slide 7
End-to-End Test Flow
From NFC scan to data in SQLite — complete chain
1️⃣ NFC Scan
Phone reads RFID tag → extracts UID
2️⃣ Build Payload
JSON constructed: uid, type, timestamp
3️⃣ Publish MQTT
→ rfidmanager/ <uid>/telemetry QoS 1
4️⃣ Broker Routes
Mosquitto receives and forwards to subscribers
5️⃣ Subscriber
Python script receives → parses JSON
6️⃣ SQLite Store
Data persisted in rfid_readings.db for analysis
✅ How to Verify
┌─────────────────────────────────────────────────────────────────────────────────┐ │ Method │ What to check │ Pass │ ├─────────────────────────────────────────────────────────────────────────────────┤ │ Terminal: python subscr. │ See incoming messages with UID and timestamp │ ✅ │ │ Terminal: mosquitto_sub │ -v flag shows exact topic + payload │ ✅ │ │ GUI: MQTT Explorer │ Real-time tree of all topics │ ✅ │ │ App: Settings │ Broker status indicator │ ✅ │ │ SQLite: rfid_readings.db │ Query: SELECT * FROM readings; │ ✅ │ │ App: Readings screen │ Scan appears in list │ ✅ │ └─────────────────────────────────────────────────────────────────────────────────┘

## Slide 8
Quick Reference
Essential commands and configurations
📡 Connection Details
┌──────────────────────────────┐ │ Parameter │ Value │ ├──────────────────────────────┤ │ Broker IP │ 192.168.50.128│ │ Port │ 1883 │ │ Protocol │ MQTT 3.1.1 │ │ Topic root │ rfidmanager/ │ │ QoS │ 1 │ │ Auth │ None (anon) │ │ TLS │ No │ │ Keep-alive │ 30s │ │ Clean sess │ true │ └──────────────────────────────┘
🗂️ Important Files
┌──────────────────────────────────────┐ │ Path │ Purpose │ ├──────────────────────────────────────┤ │ mosquitto.conf │ │ (test/fas2-mqtt/mqtt/) │ │ │ │ test_subscriber_persist.py │ │ (test/fas2-mqtt/mqtt/) │ │ │ │ simulate_mobile_publish.py │ │ (test/fas2-mqtt/mqtt/) │ │ │ │ rfid_readings.db │ │ (data/) │ │ │ │ MQTT-Infrastruktur.md │ │ (wiki/) │ └──────────────────────────────────────┘
🧪 One-Liners
Verify broker is up: docker ps | grep mqtt Listen to everything: docker exec rfid-mqtt-test \ mosquitto_sub \ -h localhost -p 1883 \ -t "rfidmanager/#" -v Publish test: docker exec rfid-mqtt-test \ mosquitto_pub -h localhost \ -p 1883 -t "test" -m "ping" View logs: docker logs rfid-mqtt-test

## Slide 9
Questions?
RFID Manager — MQTT Test Infrastructure
Joakim • 2026-06-14